1. PASSIVE ACOUSTIC SURVEILLANCE

Passive acoustic surveillance system that we are working on is a TÜBİTAK-2209A project. As its name suggest, we aim to design a acoustic surveillance with 8 MEMS microphone. The microphones are put into circular uniform area and each microphone is responsible for listening a specific direction. The PCB board also includes IMU sensor for navigation, GPS module for marking the board movements onto the map, SD card for backup, LoRa module for wireless comm and other tools for various purposes. I’m responsible for end-to-end software development so that I’m gonna give the software-specific details of this system.

1.1. Libraries

I’ve used many type of library in this project. Also I have designed two custom libraries. I will explain these in separately.

Libraries for embedded firmware:
- CMSIS (Common Microcontroller Software Interface Standard)
- HAL (Hardware Abstraction Layer)
- FreeRTOS Kernel

Libraries for ground station:
- GNU C (for standard POSIX-compatible API)
- SQLite3 (for database integration)
- Shumate (for mapping)
- Cairo (for 2D plotting)
- GTK 4 and Adwaita (for UI and main application)
- GNU GSL (for numeric computations)
- Custom DSP toolkit (will be explain below)
- Custom linear algebra toolkit (will be explain below)

1.1.1. DSP (Digital Signal Processing) Library

I’ve designed a custom DSP library for this project. The main reason of this choice is that passive acoustic surveillance requires some kind of special algorithms like beamforming, direction of arrival or specific filter designs. So this custom library was designed with these considerations.

This library includes the following modules:
- core (for the main time and frequency domain operations)
- filter (for FIR and IIR – based filter designs)
- signal (for common signal generations)
- transform (for time-frequency domain transformations)
- plot (for 2D signal plotting)
- window (for windowing operations)
- beamform (for beamforming operations)
- arrival (for direction/angle of arrival operations)

Each module is grouped with associated prefix like dsp_transform_dft(), dsp_filter_fir_low_pass() or so on. Also each data in any kind of signal is being represented as double and dynamic allocation memory is not being used at all. So that each signal is defined in stack. This is required for deterministic behavior. Figure 1.1. and Figure 1.2. shows the example usage.

   Figure 1.1. Code snippet for plotting sine

Figure 1.2. Result of the code snippet

This custom library was directly embedded into the ground station codebase. After the microphone outputs are captured from the serial port, the ground station makes required analysis using this custom library.

The project link: https://github.com/CanGulmez/Digital-Signal-Processing

1.1.2. ALAT (Advanced Linear Algebra Toolkit) Library

I’ve wrote this custom linear algebra library independently from passive acoustic surveillance project. But I noticed that this project also requires the numeric computations. After that I’ve included this library into the this project.

As being custom DSP library, each data was defined as double and the library object is being defined in stack. So that this behavior provides determinism also.
This custom library includes the following modules:
- matrices (for matrix operations)
- vectors (for vector operations)
- complexes (for complex-number operations)
- crypts (for encoding/decoding messages)
- apps (for some real-world applications)

This library also includes the GUI script to use the library easily. Figure 1.3 shows an example usage.

     Figure 1.3. Creating a random matrix

This library is not being directly embedded into the ground station. Because it has separate CLI and GUI tools. So it can be thought the complementary program to the main ground station.

The project link: https://github.com/CanGulmez/ALAT

1.2. Embedded Firmware

Embedded firmware was written for STM32H7x series microcontroller using FreeRTOS kernel. It’s designed in modular design. This is achieved over abstraction hardware layer. Its codebase includes the hardware configuration macros like initGPIO, initSPI, initDFSDM, or so on. The embedded firmware includes these component’s settings:

- LoRa module (for wireless communication)
- GPS module (for marking the movements of board onto map)
- IMU sensor (for detecting acceleration and rotation of board)
- SD card (for backup of critical data)
- MEMS microphone (for collecting the audio data around board)

Ground station supports three communication ports (I will explain later) but current embedded firmware sends the payload data over wireless, LoRa, communication. It uses UART peripheral.
Embedded firmware parses the NMEA sentences coming from GPS module and then extract the predefined data using these sentences. These data are UTC time, latitude, longitude, fix quality, number of satellite used, altitude, status, speed over ground (knots), course over ground (degrees) and data. It uses also UART peripheral.

The board includes the IMU sensor too. It’s used for navigation in the ground station. Embedded firmware reads and interprets this sensor and then put the interpreted data (in case, accelerometer and gyroscope outputs) into payload data structure. It’s done over SPI interface. In ground station, these are shown in 2D plot.

SD card is used to store the critical data when the power is off suddenly or abnormally. Embedded firmware writes the data with a fixed interval time. It’s widely used and recommended techniques in the critical system designs.

The most important mission of this system is to collect the audio data around the board simultaneously coming from MEMS microphones. It’s done overDFSDM peripheral. The embedded firmware just is responsible for packing these data into payload structure. The required analysis and operations will be taken in ground station. Because it is computationally heavy process for microconroller.

As can be seen, there are many tasks to cooperate the embedded firmware have to do. So the embedded firmware uses the FreeRTOS kernel to create, manage, schedule required tasks. Total 12 tasks are being used for these operations.

1.3. Ground Station

1.3.1. Microphone Module

1.3.2. AI Model Module

1.3.3. Navigation Module

1.3.4. GPS Map Module

The project link: https://github.com/CanGulmez/Passive-Acoustic-Surveillance